## Slide 1: International Standards Assessment Forum (ISAF)
IEA Wind TCP Task 41
Work Package #1 – Standards Development
26-28 June 2019
Dundalk, Ireland

## Slide 2: IEC 61400-2 Challenges
Incorrect characterization of wind, vertical wind speed, normal turbulence model, turbulence intensity of typical sites
Duration test impedes market access and innovation
Power performance test results give highly optimistic production estimates
Simplified Load Method (SLM) isn’t linked with turbulence intensity and doesn’t have a fatigue load case.
No fatigue load cases that cover known anecdotal failures, blade/rotor
Lack of clarity on how to use IEC 61400-13
No VAWT specific SLM, requiring the use of aeroelastic models for typically very small turbines
Turbine/tower dynamics and interactions
Complications of requirements based on turbine sizes
Notes: T

## Slide 3: ISAF Participants
Mauro Peppoloni – Austria, University of Applied Sciences Technikum Wien
Tonny Brink – Denmark, Nordic Folkecenter for Renewable Energy
Immanuel Dorn and Sudheesh Sureshkumar – Germany, Enbreeze
Raymond Byrne and Paul MacArtain – Ireland, Dundalk Institute of Technology
Seokwoo Kim - Republic of Korea, Korea Institute of Energy Technology Evaluation and Planning
Ignacio Cruz - Spain, CIEMAT
Chunto Tso and Chung-Chun Hsu (Wallace) – Taiwan, Taiwan Institute of Economic Research
Jeroen van Dam, Robert Preus - U.S., National Renewable Energy Laboratory
Trudy Forsyth – U.S., Wind Advisors Team

## Slide 4: Proposed size: Micro Wind
Size: Less than 3-5 m2or 800W – 2 kW
Electrical output: Battery charging only
Installation: Owner installed
Loads: Simplified Loads or see if assume 300 Nm covers it? Validation using Primus, other micro turbines? Allow no mechanical brake
Power curve Testing: No site calibration required
Get rid of 2-4D upwind anemometer placement, replace with a specific distance
Develop another way to define anno placement for very small rotors
Don’t test past peak power
Acoustic Testing: No tonality, emissions map
Safety and Function Testing: Demonstrate power and RPM control
Blade Testing: Test blades and rotor/hub – simplified methods
Duration Testing: Can be done in parallel as other tests at different site
If no strength analyses (stress analysis and loads) do a longer duration with high winds - 9 months?
If loads done, reduced duration test - 3 months?
Develop technical baseline of duration test time, OTF, high wind speed time periods to inform standard changes.
Dynamics: May not make sense without tower
Design Class per IEC 61400-2 Turbine design class has no relevance
Develop one design class for microwind
Other: Is simpler, more cost effective method that is better than certification?

## Slide 5: Proposed Size: Small Wind
Size: 40 or 50m2 and less or 2-10/11 kW at peak power or AEP?
Electrical Output: Grid connected or battery charging (isolated/islanded grid)
Installation: Independent or OEM installers
Loads: VAWTs – develop SLM building on Task 27
  Decide if there could be a simpler approach using pre-defined load of 300 Nm
  SLM or aeroelastic loads?
  Use existing SWT SLM work and develop aeroelastic models to validate the method used.
  If use aeroelastic model, reduce duration test or blade tests
Need to develop fatigue load cases that account for gyroscopic loads
Power Curve Testing: Develop family of curves (at least two bounding conditions, one with high turbulence intensity data or invalid sector data, one with valid sector data only
capacity factor
No site calibration required
Acoustic Testing: No tonality
Blade Testing: Static
Fatigue – could be option and trade off some duration requirements, lower FoS (aeroelastic model) or SLM with higher FoS
Compare and contrast aeroelastic model results, SLM methods.
Gather duration test data and evaluate problems across the total test time.
Need to define centrifugal loads test
Duration Testing: Consider reduced high wind speed requirements based on exploration of existing data.
Get data on turbine failure as a function of duration test
Dynamics: Need to understand eigenfrequency of tower (work led by Austria)
Other: Is simpler requirement better than certification? Labeling requirement?

## Slide 6: Proposed size: Small, big Wind
Size: 40 – 50m2 or 10-100 kW or 10-125 kW or 10-150 kW?
Electrical Output: Grid connected
Installation: Professional installers
Loads: No SLM
Use aeroelastic models for all loads
Develop clear way of validating aeroelastic models
Develop fatigue case to cover gyroscopic loads
Reduced -13 loads test?
Develop recommendations for focusing loads requirements found in IEC 61400-13
Develop comparison of aeroelastic models to measurements found (Endurance, NW 100, Norventos?)
Power Curve Testing: Can power curve be used to reduced loads test requirements?
Develop family of curves (at least two bounding high turbulence intensity data, capacity factor
Can power curve be used to validate loads models?
Blade Testing: Static and fatigue test
Acoustics Testing: IEC 61400-11 with SWT Annex, no tonality
  Loads Testing: Should at least tower loads data be gathered?
  Duration Testing: Not required
  Dynamics: Develop method for dynamic analyses validated with specific data (Austria)
  Design Class: Consider reducing to 2-3 classes based on Task 27 preliminary results
  Other: Certification and testing required

## Slide 7: Duration Testing
Goal
  Broad way of assessing short-term reliability and catching liability issue.
  Maximize the benefit of duration testing by streamlining requirements based on existing data
Problem
  Long-time (6 months) period and a need for simpler procedure
  High wind speed requirements (Based on design class)(Averaging rate of 10-minutes aggravates the high wind speeds needed.)
  Doesn’t commonly link to policies , for example in Denmark
  Doesn’t always reflect challenging environmental conditions found globally
Research needs
  Analyze duration datasets
    Brent S./SWCC, NREL, TUV NEL, CIEMAT? WindTest, DNV/GL, IECRE Test Laboratory stakeholder group – identify expenses and value added
  Based on data did the SWT work well with the first hour of high winds or 25 hours or after 25 hour
    Get data from generator about failure
    Mariah made it through duration test at Windward but failed shortly after completion of the turbine - example of turbines that made it through but failed. Do we want to increase requirements that would impact the ‘good’ turbines.

## Slide 8: Duration Testing
Research needs (continued)
  Bases on existing data, is there a reasonable approach to reducing duration time period? (particularly for micro - 3 months instead of 6 months?)
    Where do they fail? What made them fail?
      Not much public information
      High winds?
      Duration – time
  Is there a conservative way to extrapolate to meet high wind requirements?
  Is there technical rationale to change the averaging time 1-min versus 10-min?
  How to get data on turbine failure as a function of duration test?
  Set baseline for off-grid duration research and testing.
  What are the design implications of new duration test requirements?
  Phased certification, safety and function, power performance and acoustics to get a ‘limited’ certification, then complete duration test.
  Do high wind speed requirements implay a need to demonstrate control?
  Gather more test data at high turbulent sites such as Beech Mountain,, simple test with kkWh meter and nearby anemometer
  Need experience with expanded and challenging environmental conditions such as dust, erosion of blades, salt water, icing, etc
Task 41 partners
  Test laboratories and certification bodies
    Spain CIEMAT data may be available, need to check with OEM and conduct site assessment
    U.S. SWCC
    U.K. TUV-NEL
  Manufacturers
    Endurance – no longer commercially available
    Enbreeze – new turbine designer

## Slide 9: Power Performance Testing
Goal
  Develop comparable results on the power produced by wind turbines. Provide a baseline for estimating annual energy production
  Provide a baseline for organizing data for acoustic testing
  Leveraging existing IEC 61400-12-1 as baseline and drafting unique requirements for distributed wind turbines
Problem
  Current certified power curves are measured in areas where wind blockages are minimized, which is typical of accredited and formal unaccredited test sites. And while this helps create comparable results for different wind turbines, it implies that consumers should see annual energy production found in unobstructed sites
  No real measured results showing range of turbine production and performance
  Current testing requires expensive instrumentation such as calibrated anemometers
Research needs
  Results should include high turbulent results found for alpha of 0.2
    An easy approach is to analyze existing data sets for data in ‘invalid sectors’
      How would invalid sector data influence the load spectrum?
    Analyze the effects of different averaging periods using existing data
  Develop a high and low turbulence intensity power curve showing a range in rating and annual energy production (city – high TI, country – low TI)
  Explore possibilities to reduce stringency for site calibration (likely a function of turbine size)
  Evaluate cost effective instrumentation and measurement strategies
Task 41 partners - test laboratories and certification bodies
    Denmark, Nordic Folkecenter
    Republic of Korea, KIER
    Spain, CIEMAT data may be available, need to check with OEM & conduct site assessment
    U.S., SWCC
  Manufacturers
    Endurance – no longer commercially available
    Enbreeze – new turbine designer

## Slide 10: Acoustic Testing
Goal
  Develop comparable results on the sound produced by wind turbines.
  Provide an emissions map per IEC 61400-11, SWT annex, a visual approach to wind turbine sound as a function of distance; something easy for consumers.
  Provide a baseline for organizing data for acoustic testing
Problem
  Should acoustics testing be done for off-grid
  Per the IEC standard, sometimes the turbine noise is unmeasurable over the background noise. How can this be handled in a more quantifiable way?
  There is a high amount of data collected, is there a way to reduce the data required?
Research needed
  Any research conducted on new methods developed should be done for all sizes (micro, small, small/big)
  Provide a baseline for organizing data for acoustic testing
  If don’t hear a specific tone, don’t need to do tonality test. When have their been tonality tests required?
  Methods needed to handle high background noise
    What is low enough level of background noise?
    Turbines can’t be heard over background noise – okay
      Exception if background noise was below XX
  In Denmark, flowing from the large wind industry there is a new requirement on Infrasound for distributed wind

## Slide 11: SLM – Fatigue, Factor of Safety and Yaw Rate
Problem
Build SLM fatigue load case to overcome the weakest part of the -2
Very high factors of safety leading turbines to be heavier and more expensive
Yaw rate requirements, while seen on free yaw turbines, are restrictively high for other designs
Research needed
Fatigue
  Needs to be different for different turbine control methods
    Low loads for pitching, active yaw turbines
      Higher loads for passive control and passive yaw
    Running off yaw
    Yaw rates
  Needs to be different for upwind/downwind
  Does SNL have coupon testing of materials used in today’s SWT blades?
    Focus on SWT likely to be commercial in the future
    Get blade sets commercially
Well behaved turbines have yaw and RPM control
  Need to design passive yaw into FAST model

## Slide 12: SLM – Fatigue, Factor of Safety and Yaw Rate (cont.)
Develop models first then test
  HAWC or FAST validation
  What are the limits of aeroelastic models?
What FoS can provide justification?
  Go with loads
Extreme Direction Change
  Check with DTU, NREL, CIEMAT on once/ 50 year extreme direction data (DTU 3rd December 1999 – vey high winds)
Partners - Turbine models with validated measurement
  Bergey 15kW (upwind, passive yaw, tail) at several different sites
    Turbulence on performance
    Fatigue cycles
    Yaw rate
  Skystream
    Aeroelastic model
    Measurements
Future common small wind turbine testing?
  Enbreeze, active yaw – install several turbines
  Huaying?
Technical partners
  Murdoch University
  DTU
  University of Newcastle – thesis
  University of Calgary

## Slide 13: Tower Dynamics and Interactions
Problem
Need to avoid resonance above 30% nominal power and RPM for 1p or all frequencies?
  Want to be overcritical versus undercritical
  Eigenfrequency of tower is more critical
Research needed
Define framework and which natural frequencies make sense
  Include NREL FAST update to include towers
Suggest identifying different requirements since don’t currently require certification
  Survivability at different WS
  Icing or other states that are easy to reach within one year at a test site
Task 41 partners
Austria, Fachoschule Teknikum Vienna

## Slide 14: FAST model
Problem
Need to develop aeroelastic modeling capabilities since will be basis for certifying small and small, big wind turbines
Research needed
Improve capabilities
  Model lattice towers
  Turbine dynamics of yawing and tower resonance
  Reflect controls found in modern wind turbines

## Slide 15: Normal Turbulence Model
  Run the proposed NTM through aeroelastic code – Jeff Minnema
  Using Bergey (15 kW) model
  AIR Breeze (1 kW)
  Enbreeze turbine (15 kW)
  Skystream turbine (2.5 kW)
Run through structural analyses
Compress the design load cases to either 1 or 2 cases based on aeroelastic modeling exercise
  Is a low wind, high turbulence site impactful?
TI should be included in SLM fatigue analyses

## Slide 16: VAWT Simplified Loads Methodology
Problem
No loads method or simplified loads methodology for VAWTs. This requires Loads testing to meet certification requirements.
VAWT manufacturers are dominantly in Asia, highlighting the need for a standards assessment forum or discussion in Asia
Research needed
Develop simplified loads methodology (SLM) for VAWTs
  Build on work done under Task 27
Discussion of VAWTs with experts on
  Annex or separate VAWT standard?
  Upper limit for VAWTs maybe 100? kW or lower – should there be a hard limit?
Task 41 partner
Taiwan Institute of Economic Research
Japan?

## Slide 17: Future actions
Look at comparison of RSA, kW, specific power, or AEP to set size boundaries
Comparing loads using SLM, and aeroelastic models
  What load cases matter?
  Fatigue implications – if using SLM, not robust enough (may depend on configuration)
  Factor of Safety
    Get input from OEMs?
    predetermined loads
    Endurance measurements exceeded aeroelastic model loads
    Davide Conti’s data – Viking
    Murdoch University – Dr. Jonathan Whale
    Samuel Evans – Newcastle University – Skystream – thesis
    David Wood – gust data
Consider fatigue analysis of gyroscopic loads for: yaw bearing (passive yaw), yaw error (active yaw), power production and fault, normal shutdown, parked (low cycle/high fatigue), different fatigue for on and off-grid turbines.
  Extensive modeling with field testing
Look at power curve data as a function of TI How to evaluate invalid sector data?
  What is the right averaging period? (1-min, 1-sec, 10-sec, 10-min, etc.)
    KIER data - better with lower averaging period
    What gets close to accurate AEP? Will shorter averages be better?

## Slide 18: Future actions (cont.)
Assess whether blade fatigue testing adds value
    Manufacturing defects or design defects?
  Gather fatigue blade test results
    turbines that fail in the field and we don’t fail them in the lab
    OR turbines that fail in the lab but don’t fail in the field.
  Rotor test for fatigue
  Taiwan – get SLM VAWT write up – could be separate annex -2 or its own document without size limits? Need research?
  Where is the cost versus value of testing?
    Measurement equipment? Theis anno?
Loads testing -13 requirement is less appropriate the smaller the turbine is
  Data from
    NW100
    Norventos
    Endurance – someone else trying this not Dean/Dave
    Windward Engineering analysis compared to measurements
    Could have data from 100 kW turbine from Korea
      Capture matrix for stall control turbines are almost the same for duration test
    Could have data from Denmark for 168 m2 VAWT

## Slide 19: Future actions (cont.)
Query certification costs and schedule to meet -1 versus -2.
  Check with Endurance, NW100, Norvento?, C&F?, XANT, data and aeroelastic models
    NPS had to add fatigue test of blades per the certification body.
Develop SLM for downwind turbines, put in annex
Yaw rate - get data, need high turbulence site (Tonny, Jeroen?, Beech mountain – turbine already installed and easy to measure?)

## Slide 20: Other Ideas
Blade test – identify a large variety of blades and test to failure
Talk with owners, how are they performing, if not failed
  Reliability database – labor intensive to develop comparable results
    NY pilot project
  Or query turbine consumers?
    Turbines in northern Ireland – medium, new and refurbished – citizen scientist – app (done in water program)

## Slide 21: Compliance to IEC 61400-13
Goal
Develop strategies and methods to get minimum loads to validate aeroelastic models.
Problem
Limited information on how to handle IEC 61400-13, how should it be used?
  Not needed for micro and small unless it is a VAWT configuration
Aeroelastic models need some sort of measurement to refine the model
Research needed
Small, big – not allowing SLM, aeroelastic models required limited loads test?
    Tower dynamics
    Active yaw and pitch – don’t require loads?
    Can we model the aeroelastic model and validate with PP and limited loads (tower loads, avoid loads on rotating frame)? Can tune aeroelastic models based on measurements? Can’t model accurately if free yaw with tower resonance? Add mass to lower frequency?

## Slide 22: Next Steps
Hold a more detailed meeting in US. – hosted at NREL?
  Build on half day meeting held in conjunction with DWEA conference
  Target key stakeholders for detailed discussion
Send out WP1 International Standards Assessment Forum results and get global feedback? Why are you not certifying? What would make things better?
  Develop simplified survey methods and use existing communication channels
    Latin American with Ignacio Cruz
    Survey monkey – developed and analyzed by Trudy (Wind Advisors Team)
  Develop a Google form for easy compilation
    Discussion of what is not working in using -2?
Work with Task 41 partners an IEC TC88 Testing Laboratory group with a face-to-face meeting
  Where are the costs in testing and certification?
  What is the percentage of level of effort by r test laboratories and certification bodies for different certification steps?

## Slide 23: IECRE SG554
Develop conformity assessment requirements
  Other tests: even being a “design standard”, IEC 61400-1 refers to other standards which in turn require additional tests. This is the case of the blade lightning protection, which is again very expensive to test, and it is clearly not reasonable to ask 10-15m, glass fibre blades with a single receptor for the same tests as 80m, carbon fibre blades with complex protection systems. - fall meeting? (Jeroen, Alistair, Class NK, Deutsch Windguard)
Need platform for wind/certification information
  Clarify what certification mean for consumer and local jurisdiction
Requirement to work with -1, need to move to higher turbine capacity limits with validated modeling requirements